## Slide 1
STAGE REVIEW · JULY 2026
MiniVLA
V3
Recovery-aware language-conditioned control with a validated clean baseline
MuJoCo / robosuite · Mac closed-loop evaluation · Cognition L40S training
Notes: [Sources]
- Original deck asset: 2026-7-22-LiuYining.pptx, slide 1.
- README.md.
- results/hpc/v3_hpc_1349625/training_metadata_v3.json.

## Slide 2
MINIVLA V3
Current system: recovery-aware multimodal control
02
1,800 demonstrations
1,200 clean + 600 targeted recovery trajectories
TASK SPACE
Red cube
Blue sphere
Green cylinder
Pick ×3 · Push ×3
MULTIMODAL POLICY
Dual-view vision
agentview + wrist
112 × 112 RGB
Language + state
DistilBERT · 5-step history
CLOSED-LOOP CONTROL
7D OSC_POSE
ΔXYZ + axis-angle + grip
20-step ACT
chunks
Replan every step · bounded history
Research goal
Measure clean performance and degradation under controlled visual, physical, scene and temporal perturbations.
Notes: [Sources]
- results/hpc/v3_hpc_1349625/training_metadata_v3.json.
- results/hpc/v3_hpc_1349625/preflight_report_v3.json.
- models/mini_vla_v2.py.
- utils/evaluation_core_v2.py.

## Slide 3
ENGINEERING EVOLUTION
Causal data and recovery drove the V2-to-V3 gains
03
Matched clean success
12.5%
75.8%
92.5%
protocol audit
97.92%
V2
Correlated batches
Initial-state scarcity
BN instability
V2.1
Interleaving + GroupNorm
Initial-state validation
Grounding rescue
V2 Clean
Causal transitions
Interaction conditioning
Release gates
Audit
Pilot protocol defects
OOD grounding drift
Recovery gap exposed
V3
Targeted recovery data
Language augmentation
HPC fine-tuning
Key lesson
Keep the proven policy, then add targeted recovery data and stricter evaluation.
Notes: [Sources]
- results/v2_1/evaluation_clean_v2_1.json.
- results/v3_tests/clean_comparison/v2_20260714.csv.
- results/v3_tests/clean_comparison/v2_20261017.csv.
- results/v3_tests/clean_comparison/v3_20260714.csv.
- results/v3_tests/clean_comparison/v3_20261017.csv.

## Slide 4
CODE ARCHITECTURE
Three files carry the current system
04
1 · collect_data_v3.py
Target-displacement recovery
Forced miss-and-retry cases
Live target re-localisation
Rejects non-causal rollouts
2 · mini_vla_v2.py
Language + dual-view tokens
5-step proprioceptive history
20-step ACT decoder
Grounding + interaction heads
3 · evaluation_core_v2.py
Closed-loop inference
Bounded temporal ensembling
Safety + action diagnostics
Failure taxonomy
Supporting modules
v2_schema.py · training_dataset_v2.py · perturbations_v2.py
Notes: [Sources]
- scripts/collect_data_v3.py.
- models/mini_vla_v2.py.
- utils/evaluation_core_v2.py.
- utils/v2_schema.py.
- utils/training_dataset_v2.py.
- utils/perturbations_v2.py.

## Slide 5
MATCHED CLEAN EVALUATION
V3 raises clean success from 92.50% to 97.92%
05
Success rate by task (%)
240 matched episodes/model · identical seeds, scenes and evaluator
97.92%
235 / 240 V3 successes
+5.42 pp
absolute gain over V2
p=.0072
exact paired McNemar test
0.725 cm
mean V3 grounding error
Remaining: Push-B distance · Push-C drift
Chart: 
| Pick A | Pick B | Pick C | Push A | Push B | Push C
V2 Clean | 90 | 100 | 97.5 | 82.5 | 95 | 90
V3 | 100 | 100 | 100 | 100 | 92.5 | 95
Notes: [Sources]
- results/v3_tests/clean_comparison/v2_20260714.csv.
- results/v3_tests/clean_comparison/v2_20261017.csv.
- results/v3_tests/clean_comparison/v3_20260714.csv.
- results/v3_tests/clean_comparison/v3_20261017.csv.
- Computed totals: V2 222/240; V3 235/240; exact paired McNemar p=0.0072.

## Slide 6
ROBUSTNESS BENCHMARKING
Clean control is validated; robustness is now the research question
06
Paired target-displacement protocol
Same task · same seed · same collision-safe direction · paired execution modes
Protocol hardening
Teleport distance is excluded from push progress; every level shares one collision-safe direction and paired scene seeds.
Next stress tests
01 Dynamic target displacement
02 Visual noise and blur
03 Physics drift + OOD distractors
04 Camera extrinsic shift
Status: no robustness claim until paired degradation curves are complete.
0 cm
Clean
2 cm
Mild
4 cm
Core
6 cm
High
8 cm
Stress
TEMPORAL
bounded action history
LATEST-ONLY
newest prediction only
Success retention
Reacquisition latency
Failure category
Notes: [Sources]
- scripts/benchmark_robustness_v2.py.
- utils/evaluation_core_v2.py.
- utils/perturbations_v2.py.
- The prior pilot curve was removed because its protocol was invalidated by later auditing.